## Slide 1: ITER Tokamak Cooling Water System Fusion Power Symposium Washington, DC Tom Coleman AREVA Federal Services December 15, 2011

## Slide 2
About AREVA
Project Scope
Accomplishments
Summary
Tokamak Cooling Water System (TCWS)

## Slide 3
World Leader in Nuclear Power
  Uranium mining to reactor design and related services to used nuclear fuel recycling
What we do in Nuclear Energy
  Uranium exploration, mining and concentration
  Uranium conversion and enrichment
  Nuclear fuel design and fabrication
  Design and construction of nuclear reactors
  Products and services for nuclear power plant maintenance, upgrades and operations
  Recycling of used nuclear fuel
  Project management and support for work in a radioactive environment
  Nuclear logistics
About AREVA

## Slide 4
Primary Heat Transfer System for ITER
  Thermal energy generated by plasma heating and neutron heat deposition
  Auxiliary heating and radiated/transported power
  Tritium and activated products
Design and Fabrication of TCWS Components
  Heat exchangers, pumps, valves, piping, tanks, pressurizers, I&C and electrical
  Over 33,000 meters of piping
Codes, Standards, and Requirements for Components
  Dual certification (ASME and EuroNorm material certification)
  U.S. commercial codes and standards (ASME, ASCE)
  French Law certification (ESPN) with Agreed Notified Body Conformity assessment
  ITER IO Quality System (safety class (SIC), seismic class (SC), quality class (QC), vacuum class (VQC) of cooling water subsystems)
Project Phases
  Preliminary design complete November 17, 2011
  Final design initiated with schedule to complete June 2013
  Fabrication and procurement following final design with final deliveries in 2020
Project Scope

## Slide 5
AREVA Federal Services LLC – All-Employee Road Show November 2010 - p.5
5
Integration with ITER IO
  Interface for system requirement with clients
  Interface with Facility and Building Design
  Totally integrated 3D Design via CATIA V5
Preliminary Design Studies
  Transient Analysis - RELAP
  System Pipe Line and Equipment Sizing – Fathom
  Piping/Stress Analysis – ANSY/SuperPipe
  RAMI/FMEA
  Human Factors Engineering
  Manufacturability and Constructability
Operating Conditions
  Range of conditions is beyond conventional power plants
Design Considerations

## Slide 6
Capacity to remove ~1 GW of power
  Integrated Blanket, Edge Localized Mode, Divertor (IBED): 880 MW combines:
    First Wall/Blanket (FW/BLK)
    Divertor (DIV)
    Edge Localized Mode-Vertical Stabilization (ELM-VS)
  Neutral Beam Injector (NBI): 85 MW
  Vacuum Vessel (VV): 10 MW
Water and gas baking, drying, water chemistry, draining
  Vacuum Vessel Water 200 C
  IBED Water 240 C
  Diverter Gas 350 C
Safety Functions
  Confinement (tritium and activated corrosion products)
  Fast Plasma Termination System Inputs
  Primary Heat Transfer System (PHTS) Isolation Valves
  Decay Heat Removal VV PHTS
Tokamak Cooling Water System Functions
6

## Slide 7: ITER TCWS Drain Tank Room Piping

## Slide 8: ITER TCWS Lower Pipe Chase Piping

## Slide 9: Piping Analysis
Piping Analysis Requirements
  All piping designed and analyzed to ASME B31.3 Code for Process Piping
  Analysis addresses thermal, deadweight, seismic and any transients such as relief valve discharge, water hammer, etc.
  Regulatory requirements for French nuclear plants as appropriate
Piping Analysis in the Drain Tank Room
  Seventy five percent (75%) of current pipe routing in this area has been analyzed and qualified to the requirements
  The piping is stiff due to limited space and subject to low seismic excitation due to its location in the lower levels of the plant resulting in few horizontal restraints
Piping Analysis in the Lower Pipe Chase
  Characterized by ring headers that include IBED, Vacuum Vessel and Drain Piping
  Greatest challenge is the high temperatures (240°C and 350°C) for baking
  All current piping configurations have been successfully qualified for the requirements

## Slide 10
AREVA Federal Services LLC – All-Employee Road Show November 2010 - p.10
Catia CMM image of TCWS with Cryostat vessel inserted

## Slide 11: In-Cryostat Piping

## Slide 12
Overview of In-Cryostat Piping, IO CMM baseline in 2011,
(Cryostat and Bioshield Omitted for Clarity of Piping)
In-cryostat Piping
Vacuum Vessel Chimney Region, CATIA CMM 2010
Design Conditions
  Large potential temperature range (in-cryostat temp of -193°C vs baking temperature >240°C of cooling water lines)
  Upset conditions at vacuum vessel chimney
  Environmental growth and movement of cryostat structure and coolant lines
  Confinement barrier required for leak protection
  In-service inspection and Loss of Coolant event leak monitoring
18 in-cryostat modules and each freeze guard assembly (FGA) comprise two sections, the in-cryostat FGA and the upper pipe bundles

## Slide 13
Contract award early 2010
Immediate Immersion into U.S. ITER and ITER IO Project Team
Staffing Complete – 90 FTEs - SMEs
  RELAP
  System engineering, discipline engineers
  RAMI/FMEA HFE
  3D design team
Design optimization
  Heat exchanger selection
  Pressure control
Meeting Schedule and Needs
  Completion of preliminary design
  Supporting long lead procurement
  Providing data needs for building interface
Accomplishments

## Slide 14
Experienced design team integrated with US ITER and ITER IO to produce preliminary design of TCWS
Challenging operating conditions for the equipment/materials to be addressed in final design
Significant future procurement opportunities exist
Summary