## Slide 1
Terrestrial Gravity
Plans at NGS
Dru Smith
Mark Eckl
Vicki Childers

## Slide 2: Airborne Survey Control
Currently with FG-5 near tarmac
  Relative meters to connect to tarmac
A-10 soon
About 2-3 / year

## Slide 3: Geoid Change Validation
Original GRAV-D plan called for modeling geoid change through gravity change,
mostly via absolute gravimetry
More recent plan is to use absolute gravity to validate geophysically-driven gravity/geoid change models
  Requires local hydrological modeling

## Slide 4: TMGO Experimentation
Table Mountain Geophysical Observatory
NGS will conduct its own research at TMGO
  Hydrologic, Gravimetric, Etc
An open invitation exists for any researchers to temporarily house gravity and other geophysical experiments at TMGO

## Slide 5
100 meters
= New Soil Moisture Probe
(proposed location)
= New CORS (proposed location)
= New Met Sensor (proposed location)
= Existing Digital Bucket Rain Gage
= Existing TMGO CORS
30 m radius
(limit of wires
that came with
probes)
= Existing loaned TRIMBLE antenna
on pillar
= Existing Superconducting Gravimeter
= Existing 2 monitor wells (defunct)

## Slide 6: TMGO Meter-checks
NGS welcomes brief visits by those whose FG-5’s or A-10’s have recently been at Micro-G for service
Provides a safe, nearby environment for checking meter after servicing, prior to shipping home

## Slide 7: Absolute Gravimeter Comparisons
Periodic comparisons (4 years?)
  N.Amer. in 2010. More open next time.
Critical now that BIPM is no longer hosting them
Reports to IAG, and consolidated metadata website
  Contribution to the A.G. Database at BKG

## Slide 8: New Instruments
A-10
  Delivery early 2011
Under consideration (out years)
  gPhone
    Portable temporary gravity studies
  CG-5
    Augment aging L/R spring meters

## Slide 9: Field Research
Geoid Slope Validation Survey (Fall 2011)
  375 km / 270 geodetic control marks
GPS, Leveling, gravity, DoVs
FG-5 at endpoints and midpoint
A-10 on each 7th pt
  Relative gravity between

## Slide 10: Standards and Specifications
Standards of Accuracy
Working Group Definition: A statistical assessment of the final calculated value of set(s) of measurements into categories that represent the known accuracy of control relative to an accepted reference (e.g., 1st order, 1st class = 20 µGals (@ 2σ level) with < 20µGal change over 5 years)
Purpose: To report to potential users the accuracy or quality categories of measurements and computations that were made to compute the published value of survey control. By knowing the quality of the published value, a user is enabled to ascertain the usefulness of the control for their purpose.

## Slide 11: Standards (FGCC 1984)
Gravity Accuracy Standards | 
Classification | Gravity Accuracy (µGal)
First-order, class I | 20 (subject to stability verification)
First-order, class II | 20
Second-order | 50
Third-order | 100

## Slide 12: Standards and Specifications
Specifications of Measurement Systems
Working Group Definition: Those elements of a survey that are considered essential for the survey to meet the standards of accuracy for a particular order/class.
Purpose: To identify and minimize errors propagated through the individual components of a measurement system and appropriately constraining the error budget to ensure that the reported final standard of accuracy is statistically valid.

## Slide 13: Specifications (FGCC 1984)
Absolute Measurements |  |  |  | 
Order Class | 1st I | 1st II | 2nd | 3rd
Standard deviation of each excepted measurement set not to exceed (µGal) | 20 | 20 | 50 | 100
Minimum number of sets/observation | 5 | 5 | 5 | 5
Maximum Difference of measurements set from mean of all measurements (µGal) | 12 | 12 | 37 | 48
Barometric pressure standard error (mbar) | 4 | 4 | - | -
Gradient Measurements |  |  |  | 
Standard deviation of measurement of vertical gradient at time of observations (µGal/m) | 5 | 5 | 5 | 5
Standard deviation of ht. of instrument above point (mm) | 1 | 1 | 5 | 10

## Slide 14: AG Database(s)
Collecting/Organizing our historic data
  Plan to contribute to BKG’s DB
Also working on
synchronizing A.G.
collection with
“OPUS-DB”