## Slide 1
Each team has their own:
  Laptop computer
  LEGO NXT robot
  USB cable
  Light paper on the table to test the robot
Sit Down in Teams of 2
Notes: 1
1

## Slide 2
Bottle Robo Sumo
with Lego NXT & RobotC
Summer 2012
Lawrence Technological University
Co-Developed by Dr. CJ Chung and Dr. Kurt Meister
Dr. Chris Cartwright

## Slide 3
LEGO NXT is an Autonomous robot
Left Motor with Rotation Sensor
Left Light Sensor
Computer
Right Light Sensor
Right Motor with Rotation Sensor
Sonar Sensor
Notes: 3
3

## Slide 4
Your first task is to make the robot
  Go forward on the light paper
    Until it gets to the edge of the paper
    And Stop
First Program
Notes: 4
4

## Slide 5
Light sensors (which are pointed down)
  Turn on a red light
  Tell the computer how bright a light they are seeing reflected back
  Function of the color of the surface and how far the surface is from the light sensors
How does the robot know it is at the edge of the paper?
Notes: 5
5

## Slide 6
Open the program Go.c
Connect your robot to the laptop
Turn on the robot
Let’s Try It!
Notes: 6
6

## Slide 7
Open a Program
Notes: 7

## Slide 8
Open Go.c
Notes: 8

## Slide 9
Ignore the Error Message
Notes: 9

## Slide 10
How to Connect Your Robot to Your Laptop
Notes: 10
10

## Slide 11
NXT Computer
Switch programs
Emergency Stop, BACK and turn off
Turn on and ENTER
Notes: 11
11

## Slide 12
Poll the Robot’s Sensors
Notes: 12

## Slide 13
View More Information
Notes: 13

## Slide 14
Setting Up the Light Sensors
Do the same thing for Sensor 3
Notes: 14

## Slide 15
Let’s See What the Robot Sees
Put one light sensor over the light paper
Put the other light sensor over the edge of the table
Notes: 15

## Slide 16
Use the Midpoint of Those Values to Decide What is Light and Dark
Insert the midpoint in Line 9 where the question marks are
Notes: 16

## Slide 17
Let’s See What the Program Does
Notes: 17
Switch to ROBOTC and explain the program
17

## Slide 19
Download Go.c to the Robot
Notes: 19
Switch to ROBOTC and explain the program
19

## Slide 20
Run the Program
Press the Orange Button 3 times
You should see Run on the display
  Don't cheat and run the program from your laptop
Put the robot on the folder
Press the Orange Button one more time to run the program
Notes: 20

## Slide 21
Did Your Robot Stop at the Edge?
If so, GREAT
  Try adjusting the variable NormalPower and see what happens
If not,
  Try running the program again while Polling the Brick CONTINUOUSLY and adjust the values
Notes: 21

## Slide 22
Now, you are ready to play RoboSumo
Just like sumo
  One robot has to push the other off the table
  Without it going off the table
RoboSumo
Notes: 22
22

## Slide 23
Just like a bat, the Sonar Sensor sends out sound waves
  By measuring how long it takes for the sound waves to be reflected back
  It knows how far away something is
It does NOT know what that “something” is
  If YOU are the closest thing in front of the robot, it will find YOU!!!
How Does the Robot Know Where the Other Robots Are?
Notes: 23
23

## Slide 24
We’ll use Light Sensors the same way we did to find the difference between the light paper and the dark table
Now, the robot is just looking for the difference between the light table and the dark edge
  Much less light is reflected back past the edge of the table
How Does the Robot Know Where the Edge of the Table Is?
Notes: 24
24

## Slide 25
Open the Program Sumo.c
Notes: 25
25

## Slide 26
Change the LightSensorThreshold
Insert the same value for LightSensorThreshold you used for Go.c
Notes: 26

## Slide 27
Let’s See What the Program Does
Notes: 27
Switch to ROBOTC and explain the program
27

## Slide 31
If you’re daring, you can adjust some of the other variables
SonarSensorThreshold
  NormalMotorPower
  HighMotorPower
Other Variables to Adjust
Notes: 31
31

## Slide 32
Download Sumo.c
Notes: 32
32

## Slide 33
If your team is ready to compete, bring your robot to the sumo tables
The display on your NXT should show sumo.c
When I say “go”, press the orange button to run your program
If we have time, the last surviving robot from each table will have a final match
Mini Sumo Competitions
Notes: 33
33

## Slide 34: Bottle Robo Sumo
The goal is to be the first robot to find the bottle and push it off the table OR
Have your robot push the opponent off the table

## Slide 35: Necessary Strategy for bottle sumo
Instead of just moving forward, how could we have the robot search for the bottle (or an opponent)?

## Slide 36: Finding Objects using Sonar Sensor
The Ultrasonic sensor uses sound waves to locate objects and determine how far they are from the robot, just like a bat!
However, it sees things in a wide angle, just like your eyes
Its “field of vision” is about 45 degrees to either side
That means it “sees” things that are not directly in front of the robot

## Slide 37: FindObject.c

## Slide 38: Problems?
Did the robot find YOU instead of the bottle?
Did the robot spin too far (slow down the power)?
Did the robot stop too soon (remember field of vision)?

## Slide 39: Some ideas to make a complete Bottle Robo Sumo program
Usually the bottle will be located in front of the robots as shown below:
Start with left x degree spin-search and right 2x degree spin-search, where x is less than 90 degrees
Whenever, it backs up, do the similar spin-search
B
R1
R2

## Slide 40: Bottle Robo Sumo Opportunities
US Open in Nov 2012
Robot Olympic in South Korea, Dec 2012
Robot Olympic in Colorado, USA, Dec 2013
…

## Slide 41
Close Go.c, Sumo.c, FindObject.c
  Do NOT save changes
Assistants Will Close Your Programs
Notes: 41
41

## Slide 42
Between Groups
Make sure correct NXT is matched with laptop
Check the battery level on the NXTs
  Replace the battery pack if less than ½ charged
  Put the old battery pack on the charger
Make sure students didn't save programs
  If so, open copy and save as
Help the students assemble in teams of 2
Notes: 42