## Slide 1
A Taxonomy of Definitions for
Usability Studies in Biometrics
Brian Stanton
Notes: Why would someone need a set of definitions?
Height study
To summarize, the following conclusions can be reached, given a 6-inch scanner:
1. Thirty-six inches is the most efficient work surface height (i.e., lowest average
capture times). for a capture sequence that includes the right slap.
2. Twenty-six inches is the most effective (i.e., highest average image quality) heights
for a capture sequence that includes simultaneous thumbs and a left slap.
3. Users are most satisfied with a work surface height of 32 or 36 inches.
4. Start the sequence with the right hand.
5. Capture individual thumbs instead of simultaneous thumbs.
Given all considerations, placement of a scanner on a 42 inch work surface or higher
Not complete set

## Slide 2
Context of use
User satisfaction
Ease of use
Capture Threshold
Polling
Sample
@&#*%
Notes: When we got together to plan the study we didn’t understand each other
Usability:
Context of use
User satisfaction
Ease of use
Biometrics
Capture threshold
Polling
sample

## Slide 3: Traditional Fingerprint System View
Opportunity (“please place your hand on the scanner”)
System starts capture
Capture
System ends capture
Capture thresholding
Time
System
System accepts/rejects sample
Notes: When we spoke to our biometric teammates this is what we heard

## Slide 4: Digital Fingerprinting
User
Operator
Scanner
Notes: This is how a usability person would describe the fingerprinting process

## Slide 5: Holistic System View
Opportunity (“please place your hand on the scanner”)
System starts capture
Capture
System ends capture (“Please remove hand from scanner”)
Capture thresholding
Time
System
User places hand on scanner
User removes hand from scanner
User
System accepts/rejects sample
Notes: So we brought the two sides together

## Slide 6: Holistic System View
Demographics
  Age
  Gender
  Height
  Experience
  Ability
Time
System
User
Instructions
Anthropometrics
Affordance
Accessibility
Opportunity (“please place your hand on the scanner”)
System starts capture
Capture
System ends capture (“Please remove hand from scanner”)
Capture thresholding
User places hand on scanner
User removes hand from scanner
System accepts/rejects sample
Notes: Not that we have an holistic view there are items on both sides of the arrow that can affect the collection of a sample
Anthropometrics is the study of the dimensions of the human body
Affordance: the inherent characteristics of an item that communicates how to use it
Now that we brought the two sides together we were ready to define term and we started with the very basic

## Slide 7
Presentation: The display of biometric characteristics to a sensor.
A user may present multiple characteristics simultaneously
Simultaneous presentations are not necessarily constrained to any particular specific biometric modality
Notes: 4 fingerprints at once
Eyes and face
Our definitions are in general terms so that the specific meaning can be defined by the application

## Slide 8
Presentations may be further qualified as explicit or implicit
explicit presentation is a presentation that the presenter provides with their awareness
User
Operator
Scanner

## Slide 9
Presentations may be further qualified as explicit or implicit
explicit presentation is a presentation that the presenter provides with their awareness
implicit presentation is a presentation that the presenter provides without their awareness

## Slide 10
Presentations may be further qualified as cooperative or uncooperative
Cooperative presentation is a presentation that the presenter provides willingly
Uncooperative presentation is a presentation that the presenter provides unwillingly

## Slide 11: So what happens around a Presentation
Time
System
User
?
?
?
Presentation
Notes: Did the user follow instructions
Did the system think the sample was OK
Can the user do anything else but present?
So we needed a term for what happens when someone
Has the opportunity to present

## Slide 12: An Attempt is a response to an opportunity to make a presentation
Place right hand on scanner
Time
Attempt
Opportunity
Presentation

## Slide 13: A presentation may span multiple attempts
Place left hand on scanner
Place your right hand on scanner
Time
Attempt 1
Opportunity1
Presentation
Opportunity2
Attempt 2
Notes: Show why an attempt is different from an attempt
Since an attempt is the response to an opportunity
“not removing their hand” is the attempt

## Slide 14: A user may respond to a presentation opportunity with a lack of presentation
Place right hand on scanner
Time
Attempt 1
Opportunity1

## Slide 15
An attempt may be further qualified as acceptable or unacceptable
Acceptable attempt is an attempt that fulfills the minimal capture requirements of a system. Acceptable attempts must yield the minimum required biometric data from a working system in a particular configuration
Unacceptable attempt does not fulfill the minimal capture requirements of a system
Notes: By using these terms we allowed ourselves to define what the minimum
Required data, what a working system was and what the configuration is
By doing this, we can define the experimental conditions for various tests

## Slide 16: Unacceptable/Acceptable Attempts
Acceptable
Unacceptable
Place right hand on scanner
Attempt
Opportunity
Presentation
Notes: So we’ve defined if the system if the system thinks the sample is ok
But what if the user didn’t follow instructions?

## Slide 17
A task is a set of user behaviors that defines an attempt.
An attempt may also be qualified with respect to its conformance or non-conformance to a task.
Conformant attempt is an attempt that fulfills the requirements set out by a task.
Non-conformant attempt is an attempt that does not fulfill the requirements set out by a task.

## Slide 18: Conformant/Non-Conformant Attempts
Place
your
right hand
on the scanner
= Task : Conformant
≠ Task : Non-Conformant
Attempt
Opportunity
Task:

## Slide 19: Types of Attempts
Acceptability |  | 
Conformance | Acceptable Conformant | Unacceptable Conformant
 | Acceptable Non-conformant | Unacceptable Non-conformant

## Slide 20: Acceptable Conformant Attempt
Participant A presents a right hand to the fingerprint sensor, which the system detects and approves.
The user behavior (the presentation of the right hand) yields an attempt that is acceptable (the system detects and approves the data) and conformant (the user fulfilled the right hand task).
Conformant
Acceptable
Attempt
Task: “Place your right hand on the scanner”

## Slide 21: Unacceptable/Conformant Attempt
Participant B also presents a right hand to the fingerprint sensor, but the system rejects it.
The user behavior yields an attempt that is unacceptable (it was rejected) yet conformant (the user presented the right hand as they were instructed)
Conformant
Unacceptable
Attempt
Task: “Place your right hand on the scanner”

## Slide 22: Acceptable/Non-conformant Attempt
Participant C presents a left hand to the fingerprint sensor, which the system approves.
The fingerprint scan is acceptable (it was approved) but non-conformant, since the user behavior (the left hand) did not fulfill the task requirements
Non-conformant
Acceptable
Attempt
Task: “Place your right hand on the scanner”

## Slide 23: Unacceptable/Non-conformant Attempt
Non-conformant
Unacceptable
Attempt
Task: “Place your right hand on the scanner”
Participant D is distracted and makes no presentation to the fingerprint sensor and the system “times out”—i.e., no biometric data was collected within a specified interval.
This attempt is unacceptable (no hand was detected on the scanner) and non-conformant (the response to the presentation opportunity was to do nothing).

## Slide 24: Terms
Presentation
  Explicit
  Implicit
  Cooperative
  Uncooperative
Task
Attempt
  Acceptable
  Unacceptable
  Conformant
  Non-conformant

## Slide 25: Taxonomy can be found at:
Usability and Biometrics websitehttp://zing.ncsl.nist.gov/biousa/
Thank you