## Slide 1
CEBAF Polarized Electron Source:
Outlook & Horizon
Operations Group Meeting
May 13th & 20th, 2009
Joe Grames
M. Poelker, P. Adderley, J. Clark, J. Grames,
J. Hansknecht, M. Stutzman, R. Suleiman
Graduate Students: J. Dumas, J. McCarter, K. Surles-Law

## Slide 2
Following the summer SAD we begin a series of experiments with very demanding requirements of the polarized source (and of the accelerator too!)
These so-called “parity violation” experiments aim to measure tiny physics dependent asymmetries in the scattering of polarized electrons from their targets.
1,000,000
500,001
499,999
Asymmetry = D / S = (500,001 – 499,999) / (1,000,000) = 2 ppm

## Slide 3
Polarization Experiments
The common technique you’ll find for learning the spin physics interaction is to reverse the sign of the beam (or target) polarization and measure the relative difference in detected signal:
For most experiments the z-component is important. This explains why:
  Experiments need longitudinal beam polarization.
  The word helicity is used (spin parallel/anti-parallel momentum).
Aexp =
(R+ - R-)
(R+ + R-)
= Aphysics • Pbeam • Ptarget
Flip one or other…

## Slide 4
So, if R+ or R- changes because of anything other than the spin physics of the interaction, it is a false asymmetry. This results in the seemingly unattainable, golden rule for parity experiments:
No beam property other than the beam polarization should change when the beam polarization reverses sign.
But, beam properties do change:
  Intensity (first order)
  Position (second order)
  Energy (second order)
The Imperfect World
These come in different ways:
  Laser light
  Photocathode
  Accelerator
These happen before the
electrons are even a beam…

## Slide 5
Experiment | Hall | Start | Energy (GeV) | Current (µA) | Target | APV | Charge Asym (ppm) | Position Diff (nm)
HAPPEx-III | A | Aug 09 | 3.484 | 85 | 1H (25 cm) | 16.9±0.4 (ppm) |  | 
PV-DIS | A | Oct 09 | 6.068 | 85 | 2H (25 cm) | 63±3 (ppm) |  | 
PREx | A | March 10 | 1.056 | 50 | 208Pb (0.5 mm) | 500±15 (ppb) | 0.1 | 2
QWeak | C | May 10 | 1.162 | 180 | 1H (35 cm) | 234±5 (ppb) | 0.1 | 2
Overview of remaining 6 GeV “PV” Program

## Slide 6
Accelerator
A HC position difference on ANY aperture results in a HC intensity asymmetry. (Note we use absolute difference for position and relative asymmetry for intensity).
Apertures (Profile & Position):
  Emittance/Spatial Filters (A1-A4)
  Temporal Filter (RF chopping apertures)
  Beam scraping monitors.
  Any piece of beampipe!
  The small apertures and tight spots (separation?)
Adiabatic damping of the beam emittance may gain factors of 10-20 because of the reduction in amplitude of the beam envelope.
Poor optics can reduce this gain by 10x.
Poor optics stability can vary response between source and user.

## Slide 7
Chart: Bunchlength Vs Gun Voltage
| 50 | 100 | 150 | 200
200KeV | 51.5 | 56.2 | 60.2 | 64.1
115KeV | 55.7 | 68.4 | 78.7 | 87.5
100KeV | 58.4 | 73.7 | 85.7 | 95.7
85KeV | 62.7 | 81.1 | 95.2 | 99.8
70KeV | 68.2 | 91.7 | 103.4 | 105.5
Chart: Electron Bunchlength vs Gun Voltage
| 0.8 | 12 | 51 | 98 | 148 | 198
115kV | 43.771 | 60.6061 | 104.3771 | 138.0471 | 161.6162 | 188.5522
100kV | 43.8596 | 70.1754 | 96.4912 | 125.731 | 149.1228 | 152.0468 | 181.2865 | 198.8304 | 213.4503 | 233.9181
85kV | 53.8721 | 77.4411 | 107.7441 | 144.7811 | 158.2492 | 181.8182 | 208.7542 | 232.3232 | 255.8923 | 269.3603
70kV | 50.8547 | 77.7778 | 113.6752 | 152.5641 | 173.5043 | 203.4188 | 227.3504 | 245.2991 | 260.2564 | 278.2051
Measurements at CEBAF/JLab
PARMELA Simulation Results
Benchmarking PARMELA Simulation Results Against Beam-Based Measurements at CEBAF/Jefferson Lab – work of Ashwini Jayaprakash, JLab
Message: Beam quality, including transmission, improves at higher gun voltage
Chart: Transmission vs Gun Voltage
| 11.7 | 26 | 51.4 | 74.8 | 98.2 | 122.2 | 148 | 170.5 | 198
115kV | 96.5812 | 92.6923 | 82.4903 | 73.262 | 67.0061 | 61.784 | 57.6351 | 54.8974 | 51.3131
100kV | 99.0099 | 92.7419 | 77.8431 | 66.7553 | 59.2 | 52.7911 | 47.451 | 44.2153 | 40.5941
85kV | 93.8931 | 83.274 | 67.2761 | 56.2421 | 47.6465 | 40.9161 | 35.0449 | 30.9244 | 27.2059
70kV | 77.2727 | 61.6327 | 45.2479 | 35.9712 | 29.0608 | 23.7197 | 19.8027 | 17.2973 | 14.5238
Chart: Transmission Vs Gun Voltage
| 50 | 100 | 150 | 200
200KeV | 97.9 | 97.7 | 97 | 96.6
115KeV | 93.7 | 86.6 | 77.8 | 69.9
100KeV | 92.6 | 78.4 | 67.4 | 60.3
85KeV | 85.6 | 66.7 | 57.3 | 50.9
70KeV | 72.5 | 54.5 | 46.2 | 39.6
Similar Trends

## Slide 8
Load-Lock Gun at CEBAF since July 2007
  Multiple pucks (8 hours to heat/activate new sample)
  Suitcase to add new photocathodes (one day to replace all pucks)
  Mask to limit active area, no more anodizing
  Vacuum features; NEG coated, smaller surface area, vacuum fired for low out-gassing rate, HV chamber never vented
CEBAF LLGun Features

## Slide 9
Lifetime with Large/Small Laser Spots
Tough to measure >1000 C lifetimes with 100-200 C runs!
5
15
1500
350
2
≈ 18
Expectation:
“Further Measurements of Photocathode Operational Lifetime at Beam Current > 1mA using an Improved 100 kV DC High Voltage GaAs Photogun,” J. Grames, et al., Proceedings Polarized Electron Source Workshop, SPIN06, Tokyo, Japan
This result frequently cited in support of plans for eRHIC at >25mA

## Slide 10
1mA at High Polarization*
Parameter | Value
Laser Rep Rate | 499 MHz
Laser Pulselength | 30 ps
Wavelength | 780 nm
Laser Spot Size | 450 mm
Current | 1 mA
Duration | 8.25 hr
Charge | 30.3 C
Lifetime | 210 C
#How long at 1mA? | 10.5 days
High Initial QE
Vacuum signals
Laser Power
Beam Current
* Note: did not actually measure polarization
# prediction with 10W laser

## Slide 11
However, we never achieved good lifetime in tunnel…
Ultimately, we believe this is a consequence of field emission.

## Slide 12
We believed we had identified a leading suspect…
…modified a HV chamber, commissioned at Test Cave, and installed this past SAD…

## Slide 13
Field Emission – Most Important Issue
Flat electrodes and small gaps not very useful
Want to keep gun dimensions about the same – suggests our 200kV gun needs “quiet” electrodes to 10MV/m
Chart: Gradient (MV/m)
| 5.1040009799681796 | 5.5587210672744449 | 6.0134411545807014 | 6.5145612507957473 | 6.9739213389928993
50mm | 0 | 3 | 13 | 45 | 125
40mm | 0 | 0.7 | 5.5 | 20 | 65 | 170
30mm | 0 | 1.5 | 5 | 31 | 125 | 335
20mm | 0 | 4 | 16 | 65 | 220 | 475
10mm | 0 | 3 | 11.5 | 60 | 150 | 350
4mm | 0 | 4 | 18 | 30 | 65 | 390
Chart: Voltage (kV)
| 110 | 119.8 | 129.6 | 140.4 | 150.30000000000001
50mm | 0 | 3 | 13 | 45
40mm | 0 | 0.7 | 5.5 | 20 | 65 | 170
30mm | 0 | 1.5 | 5 | 31 | 125 | 335
20mm | 0 | 4 | 16 | 65 | 220 | 475
10mm | 0 | 3 | 11.5 | 60 | 150 | 350
4mm | 0 | 4 | 18 | 30 | 65 | 390
Stainless Steel and Diamond-Paste Polishing Good to ~ 5MV/m and 100kV.
Work of Ken Surles-Law, Jefferson Lab
5MV/m
100kV

## Slide 14
Let’s return to the Higher Voltage Gun…
Helps achieve ALL goals….
More UP time at CEBAF, better beam quality for Parity Violation experiments
Longer lifetime at high average current (good for FEL and positron source)
Emittance preservation at high bunch charge and peak current
High Voltage Issues:
Field emission
  Electrode design: reducing gradient and good beam optics
  Hardware limitations at CEBAF (Capture, chopper)
  Improve Vacuum
  Ion pumps
  NEG pumps
  Outgassing
  Gauges

## Slide 15
“Inverted” Gun
e-
Present Ceramic
Exposed to field emission
Large area
Expensive (~$50k)
Medical x-ray technology
New design
New Ceramic
Compact
~$5k
Want to move away from “conventional” insulator used on all GaAs photoguns today – expensive, months to build, prone to damage from field emission.
neg modules

## Slide 16
Replace conventional ceramic insulator with “Inverted” insulator: no SF6 and no HV breakdown outside chamber
Conventional geometry: cathode electrode mounted on metal support structure
Single Crystal Niobium:
Capable of operation at higher voltage and gradient
Buffer chemical polish (BCP) much easier than diamond-paste-polish
Work of Ken Surles-Law, Jefferson Lab
Chart: BCP Niobium vs Stainless Steel
| 150 | 160 | 170 | 180
niobium | 0 | 1.5 | 12 | 32
304 SS | 0 | 3 | 13 | 45 | 125
304 SS #2 | 0 | 0.7 | 5.5 | 20 | 65 | 170
Thanks to P. Kneisel, L. Turlington, G. Myneni

## Slide 17
So, our gun plans are…
  repair, test the original LL GUN (back in the Test Cave)
  build a new inverted style gun (working beginning in EEL/Test Cave)
  continue HV modeling gun for acceptable gradient/geometry
  preparing new SS and Niobium electrodes for inverted gun
  install new 150kV PS
Our plans are to install and operate higher voltage inverted gun, using existing preparation chamber, this summer.
The horizon is … NOW
…and if that’s not enough….
The PREX experiment requires the ability to flip the electron polarization 180 degrees. Our plan is to do this with a new, second Wien filter & spin rotation solenoid magnet….

## Slide 18
Summer ‘09 SAD
Install “Inverted” HV chamber with capabilities for higher voltage, anticipating better transmission & photocathode lifetime
Same good photocathode PREP and LOAD chambers
Spin Flipper: Stage 1
Remove unbaked girder region between valve & chopper
Install new “normal” Wien for Physics program, with quad correction
Thoroughly test & transfer functionality for setting pol.
No need to move laser room.
Preserve baked region, continue R&D/BS during Fall
H-Wien + Quads
Harp/A2 “match point”

## Slide 19
Winter ‘10 SAD
Same good photocathode PREP and LOAD chambers
Same “Inverted” Gun, tested at higher voltage
Same Wien filter to set longitudinal polarization for Physics
Spin Flipper: Stage 2
Replace baked region with spin flipper (vertical Wien filter + solenoid(s).
May be tilted pole Wien designed specifically for 90 deg operation at given known gun voltage
Spin Flip
V-Wien
Harp “match point”
Spin Flip Solenoid
H-Wien + Quads
Harp/A2 “match point”

## Slide 20
The End
(unless you want a few more slides…)

## Slide 21
Source Property | E-166 Experiment PRL 100, 210801 (2008) | J. Dumas et al. Proc. Spin 2008
Electron beam energy | 50 GeV - Undulator | 10 MeV - Conversion
Electron beam polarization | Unpolarized | 85%
Photo Production | Synchrotron | Bremsstrahlung
Converter Target | Tungsten Foil | Tungsten Foil
Positron Polarization | 80% (measured) | 40% (Simulation)
PhD Thesis: Polarized Positrons for JLab, Jonathan DUMAS
Advisors: Eric Voutier, LPSC and Joe Grames, JLab
ILC Polarized e+ Schemes/Demos
(synchrotron/Compton polarized photon)
Conventional un-polarized e+ Scheme
(bremsstrahlung photon)
High Polarization, High Current e- Gun
(polarized bremsstrahlung photon)
OR
Positron Yield scales with Beam Power
Replace GeV-pulsed with MeV-CW
Reduce radiation budget
Remain below photo-neutron threshold
Bunch/Capture to SRF linac
Compact source vs. Damping Ring
Unique capabilities
First CW source with helicity reversal
T. Omori, Spin 2006
E = 50 GeV L = 1m E-166 Experiment

## Slide 22
Proof of Principle Experiment: extendible to higher energy (& yield)
Precision Electron
Spectrometer (~3%)
Precision Electron
Mott Polarimeter (~1%)
e-
g
e+
e-
Pair
Brem
CEBAF Electron Source
High-P (~85%), High-QE (~3mA/500 mW)
e- bunch: 3mA @ 1497MHz demonstrated
Thesis: duty factor => low power, high peak
MeV-Accelerator
Cryounit tested to ~8 MeV
G0 setup  1.9mA @ 1497 MHz
e+ Spectrometer
(or e- & no spin rotation)
Transmission Polarimeter (MIT loan)
Conversion Target
(Tilted/Normal Tungsten Foils)
DQ = ±20
DQ = ±10
DQ = ±5
Collimators
g
Analyzer magnet
Spec.
Dipole#2
Spec.
Dipole#1
Sweep
Dipole
e+
e- after target
not shown
e-
g
g converter
DE = ±250 keV, DF = 2π
Geant4
simulation
Geant4
simulation
G4 Beamline
simulation

## Slide 23
The Source Group hosted two recent workshops:
PESP2008 – Workshop on Polarized Electron Sources and Polarimeters
JPOS09 – International Workshop on Positrons at JLab.