## Slide 1: Flat Datacenter Storage Microsoft Research, Redmond
Ed Nightingale, Jeremy Elson
Jinliang Fan, Owen Hofmann, Jon Howell, Yutaka Suzue

## Slide 3
Fine-grained write striping  statistical multiplexing  high disk utilization
Good performance and disk efficiency
Writing

## Slide 4
High utilization (for tasks with balanced CPU/IO)
Easy to write software
Dynamic work allocation  no stragglers
Reading

## Slide 5
Easy to adjust the ratio of CPU to disk resources

## Slide 6
Metadata management
Physical data transport

## Slide 7: FDS in 90 Seconds
FDS is simple, scalable blob storage; logically separate compute and storage without the usual performance penalty
Distributed metadata management, no centralized components on common-case paths
Built on a CLOS network with distributed scheduling
High read/write performance demonstrated (2 Gbyte/s, single-replicated, from one process)
Fast failure recovery (0.6 TB in 33.7 s with 1,000 disks)
High application performance – web index serving; stock cointegration; set the 2012 world record for disk-to-disk sorting
Outline

## Slide 8: Outline
FDS is simple, scalable blob storage; logically separate compute and storage without the usual performance penalty
Distributed metadata management, no centralized components on common-case paths
Built on a CLOS network with distributed scheduling
High read/write performance demonstrated (2 Gbyte/s, single-replicated, from one process)
Fast failure recovery (0.6 TB in 33.7 s with 1,000 disks)
High application performance – set the 2012 world record for disk-to-disk sorting

## Slide 9
// create a blob with the specified GUID
CreateBlob(GUID, &blobHandle, doneCallbackFunction);
//...
// Write 8mb from buf to tract 0 of the blob.
blobHandle->WriteTract(0, buf, doneCallbackFunction);
// Read tract 2 of blob into buf
blobHandle->ReadTract(2, buf, doneCallbackFunction);
Client

## Slide 10
Clients
Network
Tractservers
Metadata Server

## Slide 11: Outline
FDS is simple, scalable blob storage; logically separate compute and storage without the usual performance penalty
Distributed metadata management, no centralized components on common-case paths
Built on a CLOS network with distributed scheduling
High read/write performance demonstrated (2 Gbyte/s, single-replicated, from one process)
Fast failure recovery (0.6 TB in 33.7 s with 1,000 disks)
High application performance – set the 2012 world record for disk-to-disk sorting

## Slide 12
– Centralized metadata server
– On critical path of reads/writes
– Large (coarsely striped) writes
+ Complete state visibility
+ Full control over data placement
+ One-hop access to data
+ Fast reaction to failures
GFS, Hadoop
DHTs
FDS
+ No central bottlenecks
+ Highly scalable
– Multiple hops to find data
– Slower failure recovery

## Slide 13
(hash( ) + ) MOD Table_Size
Blob_GUID Tract_Num
Client
Metadata Server
Oracle
Tractserver Addresses
(Readers use one;
Writers use all)
Tract Locator Table
Consistent
Pseudo-random
Locator | Disk 1 | Disk 2 | Disk 3
0 | A | B | C
1 | A | D | F
2 | A | C | G
3 | D | E | G
4 | B | C | F
… | … | … | …
1,526 | LM | TH | JE
O(n) or O(n2)

## Slide 14
Extend by 4 Tracts (Blob 5b8)
Write to Tracts 20-23
Extend by 10 Tracts (Blob 5b8)
Write to Tracts 10-19
Extend by 5 Tracts (Blob d17)
Write to tracts 61-65
Write to tracts 54-60
Extend by 7 Tracts (Blob d17)
(hash(Blob_GUID) + Tract_Num) MOD Table_Size
—1 = Special metadata tract

## Slide 15: Outline
FDS is simple, scalable blob storage; logically separate compute and storage without the usual performance penalty
Distributed metadata management, no centralized components on common-case paths
Built on a CLOS network with distributed scheduling
High read/write performance demonstrated (2 Gbyte/s, single-replicated, from one process)
Fast failure recovery (0.6 TB in 33.7 s with 1,000 disks)
High application performance – set the 2012 world record for disk-to-disk sorting

## Slide 16
Bandwidth is (was?) scarce in datacenters due to oversubscription
10x-20x
CPU Rack
Top-Of-Rack Switch
Network Core

## Slide 17
Bandwidth is (was?) scarce in datacenters due to oversubscription
CLOS networks:
[Al-Fares 08, Greenberg 09]
full bisection bandwidth at datacenter scales

## Slide 18
Disks: ≈ 1Gbps bandwidth each
4x-25x
Bandwidth is (was?) scarce in datacenters due to oversubscription
CLOS networks:
[Al-Fares 08, Greenberg 09]
full bisection bandwidth at datacenter scales

## Slide 19
Bandwidth is (was?) scarce in datacenters due to oversubscription
CLOS networks:
[Al-Fares 08, Greenberg 09]
full bisection bandwidth at datacenter scales
FDS: Provision the network
sufficiently for every disk:
1G of network per disk

## Slide 20
~1,500 disks spread across ~250 servers
Dual 10G NICs in most servers
2-layer Monsoon:
  Based on Blade G8264 Router 64x10G ports
  14x TORs, 8x Spines
  4x TOR-to-Spine connections per pair
  448x10G ports total (4.5 terabits), full bisection

## Slide 21: No Silver Bullet
Full bisection bandwidth is only stochastic
  Long flows are bad for load-balancing
  FDS generates a large number of short flows are going to diverse destinations
Congestion isn’t eliminated; it’s been pushed to the edges
  TCP bandwidth allocation performs poorly with short, fat flows: incast
FDS creates “circuits” using RTS/CTS
X

## Slide 22: Outline
FDS is simple, scalable blob storage; logically separate compute and storage without the usual performance penalty
Distributed metadata management, no centralized components on common-case paths
Built on a CLOS network with distributed scheduling
High read/write performance demonstrated (2 Gbyte/s, single-replicated, from one process)
Fast failure recovery (0.6 TB in 33.7 s with 1,000 disks)
High application performance – set the 2012 world record for disk-to-disk sorting

## Slide 23: Read/Write Performance Single-Replicated Tractservers, 10G Clients
Read: 950 MB/s/client Write: 1,150 MB/s/client

## Slide 24: Read/Write Performance Triple-Replicated Tractservers, 10G Clients

## Slide 25: Outline
FDS is simple, scalable blob storage; logically separate compute and storage without the usual performance penalty
Distributed metadata management, no centralized components on common-case paths
Built on a CLOS network with distributed scheduling
High read/write performance demonstrated (2 Gbyte/s, single-replicated, from one process)
Fast failure recovery (0.6 TB in 33.7 s with 1,000 disks)
High application performance – set the 2012 world record for disk-to-disk sorting

## Slide 26
Hot Spare
X

## Slide 27
More disks 
faster recovery

## Slide 28
Locator | Disk 1 | Disk 2 | Disk 3
1 | A | B | C
2 | A | C | Z
3 | A | D | H
4 | A | E | M
5 | A | F | C
6 | A | G | P
… | … | … | …
648 | Z | W | H
649 | Z | X | L
650 | Z | Y | C
All disk pairs appear in the table
n disks each recover 1/nth of the lost data in parallel

## Slide 29
All disk pairs appear in the table
n disks each recover 1/nth of the lost data in parallel
Locator | Disk 1 | Disk 2 | Disk 3
1 | A | B | C
2 | A | C | Z
3 | A | D | H
4 | A | E | M
5 | A | F | C
6 | A | G | P
… | … | … | …
648 | Z | W | H
649 | Z | X | L
650 | Z | Y | C
M
S
R
D
S
N

## Slide 30
All disk pairs appear in the table
n disks each recover 1/nth of the lost data in parallel
Locator | Disk 1 | Disk 2 | Disk 3
1 | A | B | C
2 | A | C | Z
3 | A | D | H
4 | A | E | M
5 | A | F | G
6 | A | G | P
… | … | … | …
648 | Z | W | H
649 | Z | X | L
650 | Z | Y | C
1
2
3
1
B
C
H
M
S
R
…
…
M
S
R
D
S
N

## Slide 31: Failure Recovery Results
Disks in Cluster | Disks Failed | Data Recovered | Time
100 | 1 | 47 GB | 19.2 ± 0.7s
1,000 | 1 | 47 GB | 3.3 ± 0.6s
1,000 | 1 | 92 GB | 6.2 ± 6.2s
1,000 | 7 | 655 GB | 33.7 ± 1.5s
We recover at about 40 MB/s/disk + detection time
1 TB failure in a 3,000 disk cluster: ~17s

## Slide 32: Failure Recovery Results
We recover at about 40 MB/s/disk + detection time
1 TB failure in a 3,000 disk cluster: ~17s
Disks in Cluster | Disks Failed | Data Recovered | Time
100 | 1 | 47 GB | 19.2 ± 0.7s
1,000 | 1 | 47 GB | 3.3 ± 0.6s
1,000 | 1 | 92 GB | 6.2 ± 6.2s
1,000 | 7 | 655 GB | 33.7 ± 1.5s

## Slide 33: Outline
FDS is simple, scalable blob storage; logically separate compute and storage without the usual performance penalty
Distributed metadata management, no centralized components on common-case paths
Built on a CLOS network with distributed scheduling
High read/write performance demonstrated (2 Gbyte/s, single-replicated, from one process)
Fast failure recovery (0.6 TB in 33.7 s with 1,000 disks)
High application performance – set the 2012 world record for disk-to-disk sorting

## Slide 34: Minute Sort
Jim Gray’s benchmark: How much data can you sort in 60 seconds?
  Has real-world applicability: sort, arbitrary join, group by <any> column
Previous “no holds barred” record – UCSD (1,353 GB); FDS: 1,470 GB
  Their purpose-built stack beat us on efficiency, however
Sort was “just an app” – FDS was not enlightened
  Sent the data over the network thrice (read, bucket, write)
  First system to hold the record without using local storage
System | Computers | Disks | Sort Size | Time | Disk Throughput
MSR FDS 2012 | 256 | 1,033 | 1,470 GB | 59 s | 46 MB/s
Yahoo! Hadoop 2009 | 1,408 | 5,632 | 500 GB | 59 s | 3 MB/s
15x efficiency improvement!

## Slide 35: Dynamic Work Allocation

## Slide 36: Conclusions
Agility and conceptual simplicity of a global store, without the usual performance penalty
Remote storage is as fast (throughput-wise) as local
Build high-performance, high-utilization clusters
  Buy as many disks as you need aggregate IOPS
  Provision enough network bandwidth based on computation to I/O ratio of expected applications
  Apps can use I/O and compute in whatever ratio they need
  By investing about 30% more for the network and use nearly all the hardware
Potentially enable new applications

## Slide 37: Thank you!

## Slide 38: FDS Sort vs. TritonSort
Disk-wise: FDS is more efficient (~10%)
Computer-wise: FDS is less efficient, but …
  Some is genuine inefficiency – sending data three times
  Some is because FDS used a scrapheap of old computers
    Only 7 disks per machine
    Couldn’t run tractserver and client on the same machine
Design differences:
  General-purpose remote store vs. purpose-built sort application
  Could scale 10x with no changes vs. one big switch at the top
System | Computers | Disks | Sort Size | Time | Disk Throughput
FDS 2012 | 256 | 1,033 | 1,470GB | 59.4s | 47.9MB/s
TritonSort 2011 | 66 | 1,056 | 1,353GB | 59.2s | 43.3MB/s

## Slide 39: Hadoop on a 10G CLOS network?
Congestion isn’t eliminated; it’s been pushed to the edges
  TCP bandwidth allocation performs poorly with short, fat flows: incast
  FDS creates “circuits” using RTS/CTS
Full bisection bandwidth is only stochastic
Software written to assume bandwidth is scarce won’t try to use the network
We want to exploit all disks equally

## Slide 40: Stock Market Analysis
Analyzes stock market data from BATStrading.com
23 seconds to
  Read 2.5GB of compressed data from a blob
  Decompress to 13GB & do computation
  Write correlated data back to blobs
Original zlib compression thrown out – too slow!
  FDS delivered 8MB/70ms/NIC, but each tract took 218ms to decompress (10 NICs, 16 cores)
  Switched to XPress, which can decompress in 62ms
FDS turned this from an I/O-bound to compute-bound application

## Slide 41
2010 Experiment:
98 disks, 25GB per disk, recovered in 20 sec
2010 Estimate:
2,500-3,000 disks, 1TB per disk, should recover in 30 sec
2012 Result:
1,000 disks, 92GB per disk, recovered in 6.2 +/- 0.4 sec
FDS Recovery Speed: Triple-Replicated, Single Disk Failure

## Slide 42: Why is fast failure recovery important?
Increased data durability
  Too many failures within a recovery window = data loss
  Reduce window from hours to seconds
Decreased CapEx+OpEx
  CapEx: No need for “hot spares”: all disks do work
  OpEx: Don’t replace disks; wait for an upgrade.
Simplicity
  Block writes until recovery completes
  Avoid corner cases

## Slide 43: FDS Cluster 1
14 machines (16 cores)
8 disks per machine
~10 1G NICs per machine
4x LB4G switches
  40x1G + 4x10G
1x LB6M switch
  24x10G
Made possible through the generous support of the eXtreme Computing Group (XCG)

## Slide 44: Cluster 2 Network Topology

## Slide 45
Distributing 8mb tracts to disks uniformly at random:
How many tracts is a disk likely to get?
60GB, 56 disks:
μ = 134, σ = 11.5
Likely range: 110-159
Max likely 18.7% higher than average

## Slide 46
Distributing 8mb tracts to disks uniformly at random:
How many tracts is a disk likely to get?
500GB, 1,033 disks:
μ = 60, σ = 7.8
Likely range: 38 to 86
Max likely 42.1% higher than average
Solution (simplified): Change locator to
(Hash(Blob_GUID) + Tract_Number) MOD TableSize