## Slide 1
Mohammad Alizadeh
Stanford University
Joint with:
Abdul Kabbani, Tom Edsall, Balaji Prabhakar, Amin Vahdat, Masato Yasuda
HULL: High bandwidth,
Ultra Low-Latency
Data Center Fabrics

## Slide 2: Latency in Data Centers
Latency is becoming a primary metric in DC
  Operators worry about both average latency, and the high percentiles (99.9th or 99.99th)
    High level tasks (e.g. loading a Facebook page) may require 1000s of low level transactions
Need to go after latency everywhere
  End-host: software stack, NIC
  Network: queuing delay
This talk

## Slide 3: Example: Web Search
TLA
MLA
MLA
Worker Nodes
………
Picasso
“Everything you can imagine is real.”
“Bad artists copy.
Good artists steal.”
“It is your work in life that is the ultimate seduction.“
“The chief enemy of creativity is good sense.“
“Inspiration does exist,
but it must find you working.”
“I'd like to live as a poor man
with lots of money.“
“Art is a lie that makes us
realize the truth.
“Computers are useless.
They can only give you answers.”
1.
2.
3.
…..
1. Art is a lie…
2. The chief…
3.
…..
1.
2. Art is a lie…
3.
…..
Art is…
Picasso
Strict deadlines (SLAs)
Missed deadline
  Lower quality result
Many RPCs per query
  High percentiles matter
Deadline = 250ms
Deadline = 50ms
Deadline = 10ms
Notes: After the animation, say “this follows what we call the partition/aggregate application structure. It’s actually quite general any time you have to do distributed lookups of large data structures to resolve queries.”

## Slide 4: Roadmap: Reducing Queuing Latency
TCP
~1–10ms
DCTCP
~100μs
HULL
~Zero Latency
Baseline fabric latency (propagation + switching): ~10μs
Notes: "With TCP, queuing delays can be in the milliseconds; more than 3 orders or magnitude larger than the baseline"

## Slide 5: Low Latency & High Throughput
Data Center Workloads:
Short messages [50KB-1MB]
(Queries, Coordination, Control state)
Large flows [1MB-100MB]
(Data updates)
Low Latency
High Throughput
The challenge is to achieve both together.

## Slide 6: TCP Buffer Requirement
Bandwidth-delay product rule of thumb:
  A single flow needs C×RTT buffers for 100% Throughput.
Throughput
Buffer Size
100%
B
B ≥ C×RTT
B
100%
B < C×RTT
Buffering needed to absorb TCP’s rate fluctuations
Notes: Now in the case of TCP, the question of how much buffering is needed for high throughput has been studied and is known in the literature as the buffer sizing problem.
End with: “So we need to find a way to reduce the buffering requirements.”

## Slide 7: DCTCP: Main Idea
Source:
React in proportion to the extent of congestion
  Reduce window size based on fraction of marked packets.
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%
Switch:
Set ECN Mark when Queue Length > K.
B
K
Mark
Don’t
Mark
Notes: Start with: “How can we extract multi-bit information from single-bit stream of ECN marks?”
- Standard deviation: TCP (33.6KB), DCTCP (11.5KB)

## Slide 8: DCTCP vs TCP
Setup: Win 7, Broadcom 1Gbps Switch
Scenario: 2 long-lived flows,
(Kbytes)
ECN Marking Thresh = 30KB
Notes: Not ns2.

## Slide 9: HULL: Ultra Low Latency

## Slide 10: What do we want?
TCP:
~1–10ms
DCTCP:
~100μs
~Zero Latency
How do we get this?
C
Incoming Traffic
TCP
Incoming Traffic
DCTCP
K
C

## Slide 11: Phantom Queue
Link
Speed C
Switch
Bump on Wire
Key idea:
  Associate congestion with link utilization, not buffer occupancy
  Virtual Queue (Gibbens & Kelly 1999, Kunniyur & Srikant 2001)
Marking Thresh.
γC
γ < 1 creates
“bandwidth headroom”

## Slide 12: Throughput & Latency vs. PQ Drain Rate
Throughput
Switch latency (mean)

## Slide 13: The Need for Pacing
TCP traffic is very bursty
  Made worse by CPU-offload optimizations like Large Send Offload and Interrupt Coalescing
  Causes spikes in queuing, increasing latency
Example. 1Gbps flow on 10G NIC
65KB bursts every 0.5ms

## Slide 14: Hardware Pacer Module
Algorithmic challenges:
  Which flows to pace?
    Elephants: Begin pacing only if flow receives multiple ECN marks
  At what rate to pace?
    Found dynamically:
Outgoing Packets
From
Server NIC
Un-paced Traffic
TX
Token Bucket
Rate Limiter
Flow Association
Table
R
QTB

## Slide 15
Throughput
Switch latency (mean)
Throughput & Latency vs. PQ Drain Rate
(with Pacing)

## Slide 16
No Pacing
Pacing
No Pacing vs Pacing (Mean Latency)

## Slide 17
No Pacing
Pacing
No Pacing vs Pacing (99th Percentile Latency)

## Slide 18: The HULL Architecture
Phantom Queue
Hardware
Pacer
DCTCP Congestion Control

## Slide 19: More Details…
Application
DCTCP CC
NIC
Pacer
LSO
Host
Switch
Empty Queue
PQ
Large Flows
Small Flows
Link (with speed C)
ECN Thresh.
γ x C
Large
Burst
Hardware pacing is after segmentation in NIC.
Mice flows skip the pacer; are not delayed.

## Slide 20: Dynamic Flow Experiment 20% load
Load: 20% | Switch Latency (μs) |  | 10MB FCT (ms) | 
 | Avg | 99th | Avg | 99th
TCP | 111.5 | 1,224.8 | 110.2 | 349.6
DCTCP-30K | 38.4 | 295.2 | 106.8 | 301.7
DCTCP-6K-Pacer | 6.6 | 59.7 | 111.8 | 320.0
DCTCP-PQ950-Pacer | 2.8 | 18.6 | 125.4 | 359.9
9 senders  1 receiver (80% 1KB flows, 20% 10MB flows).
~93% decrease
~17% increase

## Slide 21
Load: 40% | Switch Latency (μs) |  | 10MB FCT (ms) | 
 | Avg | 99th | Avg | 99th
TCP | 329.3 | 3,960.8 | 151.3 | 575
DCTCP-30K | 78.3 | 556 | 155.1 | 503.3
DCTCP-6K-Pacer | 15.1 | 213.4 | 168.7 | 567.5
DCTCP-PQ950-Pacer | 7.0 | 48.2 | 198.8 | 654.7
9 senders  1 receiver (80% 1KB flows, 20% 10MB flows).
Dynamic Flow Experiment 40% load
~91% decrease
~28% increase

## Slide 22: Slowdown due to bandwidth headroom
Processor sharing model for elephants
  On a link of capacity 1, a flow of size x takes
  on average to complete (ρ is the total load).
Example: (ρ = 40%)
1
0.8
Slowdown = 50%
Not 20%

## Slide 23: Slowdown: Theory vs Experiment
Chart: Traffic Load (% of Link Capacity)
| 0.2 | 0.4 | 0.6 | 0.2 | 0.4 | 0.6 | 0.2 | 0.4 | 0.6
Theory | 0.53846 | 0.875 | 2.3333 | 0.29032 | 0.42857 | 0.81818 | 0.19 | 0.28 | 0.48
Experiment | 0.55617 | 0.89642 | 1.6445 | 0.30633 | 0.49331 | 0.82408 | 0.17295 | 0.32119 | 0.5568
DCTCP-PQ800
DCTCP-PQ900
DCTCP-PQ950

## Slide 24: Summary
The HULL architecture combines
  DCTCP
  Phantom queues
  Hardware pacing
A small amount of bandwidth headroom gives significant (often 10-40x) latency reductions, with a predictable slowdown for large flows.

## Slide 25: Thank you!