## Slide 1: RHIC Polarimetry
A.Bazilevsky
For the RHIC Polarimetry Group
RHIC&AGS User’s Meeting
May 29, 2008

## Slide 2: RHIC Polarimetry
BRAHMS & PP2PP (p)
STAR (p)
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. Proton Source
500 mA, 400 ms
Spin Rotators
Solenoid Snake
Siberian Snakes
200 MeV Polarimeter
AGS pC CNI Polarimeter
AC Dipole
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
RHIC
Siberian Snakes
Cold Snake
Warm Snake

## Slide 3: Polarization Measurements
H-Jet
Absolute polarization
p-Carbon
Polarization profile
Polarization vs time in a fill
Fill-by-fill polarizations
Local Polarimeters
Monitor spin direction at collision regions
(Confirmation of long. polarization)
Capable to monitor polarization decay vs time in a fill and bunch-by-bunch polarization

## Slide 4: HJet
Beam and target are both protons
RHIC proton beam
Forward scattered
proton
H-jet target
recoil proton
Ptarget is provided by Breit Rabi Polarimeter
<5%
Elastic scattering: Interference between electromagnetic and hadronic amplitudes in the Coulumb-Nuclear Interference (CNI) region

## Slide 5: HJet target system
RF transitions (WFT or SFT)
|1> |2> |3> |4>
Separating Magnet (Sextuples)
H2 desociater
Holding magnet
2nd RF-transitions for calibration
P+ OR P
H = p+ + e
Atomic Beam Source
Scattering chamber
Breit-Rabi Polarimeter
Separating magnet
Ion gauge
|1> |3> |2> |4>
|1> |2>
|1> |2>
Ion gauge
Hyper fine structure

## Slide 6: HJet: Ptarget
1 day
Nuclear polarization of the atoms measured by BRP: 95.8%  0.1%
Correct for H2, H2O contamination.
Ptarget = 92.4%  1.8%
Nuclear polarization
Very stable for entire run period !
Polarization cycle (+/ 0/  ) = (500/50/500) seconds
Source of normalization for polarization measurements at RHIC

## Slide 7: HJet: Identification of Elastic Events
Ch#1
source for energy calibration
241Am(5.486 MeV)
proton beam
Forward scattered
proton
proton target
recoil proton
Array of Si detectors measures TR & ToF of recoil proton.
Channel # corresponds to recoil angle R.
Correlations (TR & ToF ) and (TR & R )  the elastic process
Ch#2
Ch#3
Ch#4
Ch#5
Ch#6
Ch#7
Ch#8
Ch#9
Ch#10
Ch#11,12
Ch#13
Ch#14
Ch#15
Ch#16
Ch#1-16
R
Ch#1
#16

## Slide 8: HJet:
Example from Run6
εbeam
εtarget
Measures average over beam profile polarization with fill-by-fill stat. uncertainty ~10%
Data accumulated for a few fills provide normalization for pC polarimeter with uncertainty <5%

## Slide 9: HJet
 Run4 Blue
 Run5 Blue
 Run5 Yellow
 Run6 Blue
 Run6 Yellow
Target asymmetry vs TR
HJet performance is very stable through the Years
Background is small and doesn’t change from Year to Year, for Blue and Yellow
 Beam polarization is measured reliably by HJet

## Slide 10: Hjet: Two Beam Mode
Successfully tested in Run8
  Background level is the same as in single beam mode
  Will allow to monitor both beam polarizations by HJet simultaneously in all fills
Both beams on target
Blue beam on target
Yellow beam on target

## Slide 11: HJet: AN in pp
24 GeV: calculations with no hadronic spin flip amplitude contribution are not consistent with data
100 GeV: calculations with no hadronic spin flip amplitude contribution are consistent with data
More data to come:
24 GeV: take more data in Run9/10
31 GeV: finalize analysis of data from Run6
250 GeV: take data in Run9/10
24 GeV
100 GeV
PLB638, 450
Preliminary

## Slide 12: pC:
Ultra thin Carbon ribbon Target
(5 mg/cm2)
1
3
4
5
6
2
Si strip detectors
(TOF, EC)
18cm
Polarized proton
Recoil carbon
Carbon target
Elastic scattering: interference between electromagnetic and hadronic amplitudes in the Coulumb-Nuclear Interference (CNI) region

## Slide 13: pC: AN
zero hadronic
spin-flip
With hadronic
spin-flip (E950)
Phys.Rev.Lett.,89,052302(2002)
pC Analyzing Power
Ebeam = 21.7GeV
Ebeam = 100 GeV
unpublished
Run04
Elastic scattering: interference between electromagnetic and hadronic amplitudes in the Coulumb-Nuclear Interference (CNI) region

## Slide 14: pC: goals/strategy
Polarization measurements for experiments
  Target Scan mode
    Provides polarization at beam center, polarization profile, average polarization over profile
  20-30 sec per measurement
    For stat. precision 2-3%
  4-5 measurements per fill, per ring
    Controls polarization decay vs time in a fill
  Polarization profile, both vertical and horizontal
  Normalized to HJet measurements over many fills
    Knowledge on polarization profile in one transverse direction is required
  Fill-by-fill polarization
    Knowledge on polarization profile in both transverse directions is required
Feedback for accelerator experts
  Beam emittance measurements, bunch-by-bunch
  Polarization
  Polarization profile, both vertical and horizontal
  Polarization at injection (and polarization loss in transfer)
  Polarization on the ramp (and polarization loss during ramp)

## Slide 15: pC: polarization in a fill
Example from Run6
Fill 7820
Fill 7622
Yellow
Blue
Some fills may show polarization decay vs time

## Slide 16: pC: Polarization Profile
Target Position
Polarization
Rate
Target Position
Rate
Polarization
Beam polarization profile is different for different beams, different fills 
Correction for average polarization depends on beam/fill
Examples of pC measurements in Run5

## Slide 17: Average Polarization
H-Jet
~1 mm
6-7 mm
pC
Collider
Experiments
P(x,y) – polarization profile, I(x,y) – intensity profile
x=x0

## Slide 18: Average Polarization
If I1= I2= I
If target positioned at beam
peak intensity/polarization
pC
H-Jet
Collider
Experiment
Corrections due to polarization profiles are different when normalizing pC to H-Jet and when propagating pC measurements to experiments
Polarization profile in both trans. directions (X,Y) required

## Slide 19: pC: Polarization Profile
pC
Scan C target over the beam cross:
Target Position
Intensity
Polarization
I
P
2. Obtain R directly from the P(I) fit:



P
I
Precise target positioning is NOT necessary
1. Directly measure I and P :

## Slide 20: pC: Polarization Profile
P(L) in one fill
R=0.290.07
Run6 data: R vs fill
Vert-yellow
Vert-blue
Horiz-blue
Horiz-yellow
R~0.1–0.3  5–15% different polarization seen by HJet and by experiments

## Slide 21: pC: Polarization vs Fill
Run6 results
31 GeV
100 GeV
31 GeV
100 GeV
Normalized to Hjet
Corrected for polarization profile

## Slide 22: Hjet+pC: Run8 Analysis
Offline analysis is almost completed and results will be released soon
Fast (~online) analysis – during the run
εtarget and εbeam from HJet
Beam polarization from HJet
Beam polarization from HJet
pC-online/Jet: pC calibration
Polarization vs fill:
normalized, profile corrected

## Slide 23: pC: Upgrade
Detector upgrade
  Photo-diod instead of Si strips
Target upgrade
  Possibility of using nano-tubes under investigation
pC vacuum chamber upgrade
  Two polarimeter setups per ring
  Double number of targets (to avoid a need to open chamber to install new targets during the run)
  Reduce the time required for successive measurements of horiz. and vert. profiles
  Allows installation and testing new detectors for higher rate capabilities

## Slide 24: PHENIX Local Polarimeter
Utilizes spin dependence of very forward neutron production (PLB650, 325):
neutron
charged
particles
ZDC (energy) + SMD (position)
SMD
ZDC

## Slide 25: PHENIX Local Polarimeter
Blue
Yellow
Blue
Yellow
Blue
Yellow
Spin Rotators OFF
Vertical polarization
Spin Rotators ON
Correct Current !
Longitudinal polarization!
Spin Rotators ON
Current Reversed
Radial polarization
Asymmetry vs φ
Monitors spin direction in PHENIX collision region

## Slide 26: STAR Local Polarimeter
3.3<|h|< 5.0 (small tiles only)
Utilizes spin dependence of hadron production at high xF:
Bunch-by-bunch (relative) polarization
Monitors spin direction in STAR collision region
Capable to precisely monitor polarization vs time in a fill, and bunch-by-bunch

## Slide 27: Summary
RHIC Polarimetry consists of several independent subsystems
  Hjet:
    Absolute polarization measurements
    Absolute normalization for other RHIC Polarimeters
  pC:
    Separate for blue and yellow beams
    Normalization from HJet
    Polarization vs time in a fill
    Polarization profile
    Fill-by-fill polarizations for experiments
  PHENIX and STAR Local Polarimeters:
    Monitor spin direction (through trans. spin component) at collision
    Polarization vs time in a fill (for trans. pol. beams)
    Polarization vs bunch (for trans. pol. beams)
Reliably provides RHIC beam polarizations
  With relative uncertainty better than 5%
Continuously developing
    Detector and target system upgrade to deal with high beam intensities, and to improve efficiency and reliability

## Slide 28: Backups

## Slide 29: H-jet system
RHIC proton beam
Recoil proton
Height: 3.5 m
Weight: 3000 kg
Entire system moves along x-axis 10 ~ +10 mm to adjust collision point with RHIC beam.
IP12
target