## Slide 1: Digital RFC QPF Availability
Interagency Water Resource Meeting
March 28,2007

## Slide 2: RFCs in the Southwestern Division

## Slide 3: QPF Process
  The Hydrometorological Prediction Center (NWS national center) issues national QPF forecasts
  HPC issues 6 hour QPF forecasts out to 3 days based on guidance from the meteorological models
  RFC HAS Forecasters incorporate local expertise and latest data to refine the HPC forecast
    Coordinate with local forecast offices and HPC

## Slide 4: HPC QPF
24 Hour QPFs | 
Product | Issuance Time
94q (preliminary Day 1) | 0600Z & 1800Z
94q (final Day 1) | 1000Z & 2200Z
98q (preliminary Day 2) | 0600Z & 1800Z
98q (final Day 2) | 1000Z & 2200Z
99q (Day 3) | 0800Z & 2000Z
Forecast Discussion (QPFPFD) | 
Preliminary Day 1 | 0700Z & 1900Z
Preliminary Days 1-3 | 0900Z & 2100Z
Final Days 1-3 | 1100Z & 2300Z

## Slide 5: NMAP Program

## Slide 6: NMAP Program

## Slide 7: Adding Local Expertise

## Slide 8: RFC QPF Metrics
  Up to 72 hours of QPF generated
    Discrete 6 hour periods
    Number of periods generated dependent on issuance time and issuing RFC
  Gridded precipitation produced on 4x4 km grid (HRAP)
  NWS hydrologists normally incorporate first 1 to 4 periods (6 to 24 hours) into hydrologic models
    Dependent on RFC, type of rain event, time of year
    Up to all 12 periods (72 hours) can be used during significant events, such as tropical systems

## Slide 9: RFC QPF Availability
RFC | Regular Issuances | Number of Hours | Digital Data Available? (Where?) | Digital Format
 | Supplemental |  |  | 
ABRFC | 12z 18z 00z | 48 24 48 | Yes ABRFC web page | netCDF
 | 06z (as staffed) | 24 |  | 
LMRFC | 12z 18z 00z | 72 54 72 | Yes NWS SR Server | XMRG
 | 06z (as staffed) | 54 |  | 
WGRFC | 12z 00z | 72 72 | Yes NWS SR server | GRIB XMRG
 | 18z (flood events) 06z (as staffed) | 54 54 |  | 

## Slide 10: Digital Data Formats
  XMRG – Internal NWS format used for transferring gridded precipitation into the NWSRFS river forecast model
  GRIB – GRIdded Binary format approved by the World Meteorological Organization (WMO)
  NetCDF – Network Common Data Format developed by Unidata
  Shapefile – Standard GIS format developed by ESRI
  VGF – Vector Graphic Format used by HPC to transfer QPF to RFCs

## Slide 11: ABRFC QPF Availability

## Slide 12: WGRFC & LMRFC QPF Availability
Password protected site ftp://ftp.srh.noaa.gov/wgrfc/

## Slide 13: HPC QPF Availability
http://www.hpc.ncep.noaa.gov/qpf/

## Slide 14: HPC QPF Availability

## Slide 15: HPC QPF Availability

## Slide 16: Digital Data Formats
Questions & Discussion