## Slide 1: High Level LHC Schottky Software Development
Jerry Cai
& The LAFS Team
28 January 2009
Presented by Elliott McCrory

## Slide 2: High Level LHC Schottky Software
Initial version of High Level Software for LHC Schottky project has been completed.
Implements the requirements from:
  “4.8 GHZ Schottky Software—High Level Requirements “
  EDMS Document # 908986
  by Andreas Jansson and Dave Mcginnis of Fermilab and Ralph Steinhagen (BE/BI)

## Slide 3: Schottky Software
Integrates experience at Fermilab from the Tevatron Schottky system
It consists of two parts:
  Monitor Application
    Daemon
  Control & Display Application
    Operations GUI

## Slide 4: Design Concept: Monitor and Control & Display
Control & Display App
Schottky Front End/FESA
Device Settings
Calculation Engine
Settings & Readings Configuration DB*
Publish/ Subscribe
Logging DB
Device Readings
ModeMap
SDDS
Beam Mode
Monitor Daemon
Incl. Heartbeat
Setup Phase Only

## Slide 5: Monitor Application
Runs continuously in the background as a “Daemon Process”
Key Elements:
  Configures Schottky per Beam Mode
    See next slide
  Reads raw FFT data from Schottky
  Performs fits for:
    Tune,
    Momentum Spread,
    Emittance,
    Chromaticity, and
    Averages of these
  Publishes these results
  Archives these results
    Creates SDDS Files, post-mortem data sets and provides these data for the logging DB

## Slide 6: Daemon: Interaction with Schottky
Reacts to the Beam Mode
  The Monitor listen for changes in LHC Beam Mode
  Configures Schottky hardware based on Beam Mode
    Unique configuration table:
      One “row” of settings per LHC Beam Mode
      Each column is a settable attribute in the FESA class
        Assumes the Schottky FESA class exists!
    Control & Display GUI can change the configuration table
Is the only agent to receive raw Schottky data directly
  Republishes raw data
  Publishes calculated data
A true “daemon process”

## Slide 7: The Control and Display Application

## Slide 8: Control & Display App (1/3)
Operations GUI
Subscribes to data from the Monitor
Displays these data
  Can also display archived and post-mortem data
Two different run modes
  READ ONLY
    default
  READ and SET
    allow user to change things in the Monitor

## Slide 9: Control & Display App (2/3)
Responsible for setting up configuration table for Monitor Daemon
  Config Table:
    One row per Beam Mode
    One column per settable attribute in the hardware &/or the FESA class
  Tables are saved in SDDS files
    Would like to have a Config DB
    Monitor reads “default.sdds”
Multiple Control & Display instances?
  Each can read from the Monitor
  Only one is allowed to have setting rights at a time
    User requests setting rights from Monitor for N minutes
    RBA Login Required

## Slide 10: Control & Display App (3/3)
GUI has four sections:
  Top Tool Bar
    to exit program, read archived data ,etc.
  Left Selection Panel
    to select device and running mode
  Central Tabbed Panel
    to display data, create and load configuration tables, etc.
  Bottom Console
    to show messages while program is running

## Slide 11: Screen Shots of GUI
Tabs
  Contour and Trace
    Live or Archived data/Post-Mortem
  Time Plot
    Live or Archived data/Post-Mortem
  Electronics States/Live Schematic
  Tune Resonance Lines
  Configuration Editor
    6. Selecting bunch/gates

## Slide 12: Tab for Contour and Trace (1/6)

## Slide 13: Post-Mortem data dump (200 spectra)

## Slide 14: Tab for Time Plot (2/6)

## Slide 15: Time Plot for Post-Mortem Data

## Slide 16: Tab for Electronic States (3/6)
Active elements are colored

## Slide 17: Tab for Tune Resonance Lines (4/6)
Zoom in, using JDataViewer zooming

## Slide 18: Tab for Configuration Editor (5/6)

## Slide 19: Details of Configuration Editor
Row:
  Beam Mode
Column:
  A settable item in the Schottky front end
  On the Electronics States diagram/schematic
Can read
  Live configuration from Monitor
  SDDS save files
  History files
Can change any value in this table
  Table can be extended easily in the Java
Disposition?
  Send to Monitor
    emporarily change live table, or
    Create a new“default.sdds”
  SDDS Save File/Config DB
Invisible control: Beam gating (next slide)

## Slide 20: Bunch Gates: View and Set (Popup window, 6/6)

## Slide 21: Running the Suite
CVS Package
  lhc-daemons/lhc-daemon-schottky
Monitor Application
  Must start this first
  cern.lhc.daemon.schottky.monitor.MonitorMain.java
Control & Display Application
  cern.lhc.daemon.schottky.controller.ControlMain.java

## Slide 22: Comments
Users Guide & this talk available from Wiki
  https://wikis.cern.ch/display/LAFS/Schottky
Known limitations of this demo
  It does not connect with any LHC hardware
    No FESA class
  Daemon & GUI must be run on the same PC.
    Using SDDS files instead of a Configuration DB
  Awaiting proper “Command” communications example
    From M. Misiowiec.
  Do not run multiple Monitors at the same time, anywhere in the Control System—the subscriptions will not work properly.

## Slide 23: Summary
This initial version of high level LHC Schottky Software has implemented the elements of the requirements document.
  Monitor Process/Daemon
  Control & Display Application/Operations GUI
Improvements?
  “Configuration DB” is implemented as local SDDS files
    need BE/CO/DM help
  BE/OP feedback
  Better use of JAPC-standard communications
Issue: FESA class not yet available.
  This demo uses stored data from the Schottky monitors in the Tevatron.
Acknowledgements