## Slide 1: End plate analysis, STAR support cylinders
Feb. 2009

## Slide 2: Cone Geometry
rotational sweep
of a triangle
units: mm

## Slide 3: Single wall cone
single cone surface, cone face in slide 2
2 mm thick wall titanium (carbon composite equivalent)
100 lb load displaced by 2m from connection ring
Delta z = 200 microns
cone core-Study 4-1.htm

## Slide 4: Triangle sweep, shell mesh
Triangle sweep shown in slide 2
1 mm thick walls
Shell analysis
Fixed to edge (not surface). Rigid rod type
cone core-triangle sweep-1.htm

## Slide 5: Triangle sweep solid mesh
cone empty-Study 1-1.htm
solid mesh, same geometry as slide4
1 mm hollow
Load 100 lb at 2m
Delta Z = 228 microns

## Slide 6: Flat plate geometry
8 mm thick

## Slide 7: Flat plate, shell mesh, 8mm
flat 8 mm plate
load: 100 lb at 2 m, rigid bars on edge
Delta Z = 937 microns
Shell mesh (thick)
Titanium
cone core-flat 8 mm plate-1.htm

## Slide 8: Flat plate, solid mesh, 8 mm
flat plate
solid mesh
8 mm thick
Delta z: 1470 microns
flat plate-Study 1-1.htm

## Slide 9: Ribbed geometry

## Slide 10: Ribbed, full taper
Ribbed, full taper
solid mesh
1 mm skins
2 mm ribs
full taper
Delta Z: 1230 microns
ribbed plate-ribbed study 1-1.htm

## Slide 11: Ribbed, non tapered
full ribs
2 mm ribs
1 mm skins
Solid mesh
Delta z: 312 microns
ribbed plate non tapered 1-1.htm

## Slide 12: summary
geometry | Slide # | Mesh type | Dz | Study link
Single wall cone, 2 mm thick wall | 3 | shell | 200 m | cone core-Study 4-1.htm
Triangle sweep, 1 mm thick wall | 4 | shell | 165 m | cone core-triangle sweep-1.htm
Triangle sweep, 1 mm thick wall | 5 | solid | 228 m | cone empty-Study 1-1.htm
Flat plate, 8 mm thick | 7 | shell (thick) | 937 m | cone core-flat 8 mm plate-1.htm
Flat plate, 8 mm thick | 8 | solid | 1470 m | flat plate-Study 1-1.htm
Ribbed, full taper | 10 | solid | 1230 m | ribbed plate-ribbed study 1-1.htm
Ribbed, non tapered | 11 | solid | 312 m | ribbed plate non tapered 1-1.htm

## Slide 13: summary
Triangular swept shell is the stiffest, but only marginally
The simple single layer 2 mm cone is nearly as stiff and much simpler. It presents the same radiation length as the 1 mm triangular sweep. This solution appears to be stiff enough for coupling the STAR cylinders.
The 8 mm disk is clearly inferior for both radiation length and stiffness
The ribbed structure has ribs aligned with the TPC sector boundaries
The results are suspect because the shell mesh solutions do not agree with the solid mesh